## Slide 1: 2017 Joist
Moderator: Marvin Freeman
Presenter: Ryan Vanek

## Slide 2: Joist
BIM and System joists have been merged, taking the benefits of both
  System
    Node matching
    Framing situation
    Connection Design
  BIM
    3D Solids
    Joist shapes

## Slide 3: Joist
Jobs with joist, converted from 2016, will change the joist to the new style.
Added at bearing elevation.
New locate modifier to add at top of joist elevation.
  Display feedback to show elevation at top chord and bearing.
Shapes
  Parallel
  Single Pitch
  Double Pitch
  Arched Chord
  Bowstring
  Scissor
  Triple Pitch
  BIMCustom

## Slide 4: Joist
Panel display method
  Automatic
  Reserved
  Mfg pre-config.
  User pre-config.
Joist Manufacturer Manager
  Found in Utility Functions
  Canam
  Vulcraft

## Slide 5: Joist
Job Options – Joist Manufacture Setup
  Joist manufacturer
    Reads from Joist Manufacturer Manager
  Panel display method
  When joist manufacturer is change it will update all joist in the model that are not model complete.

## Slide 6: Joist

## Slide 7: Joist

## Slide 8: Joist
Auto standard connections
  User Interface changed
  Joists added to beam and column
Auto cap plate when joist is added to top of column.
Bolt Design Criteria
  Setup for all joist types

## Slide 9: Joist
Setbacks and Extensions
  Chord only(S type) extension
    Applies to top chord only
  Full(R type) extension
    Applies to top chord and shoe
Bearing shoe slots
  Slot diameter
  Slot length
  Slot edge distance NS and FS
Bolts
  Bolt diameter
  Distance to holes
  Gage

## Slide 10: Joist
Joist Setup found in Standard Fabricator Connections
  Bearing connections
    OSHA span for bolted connections
      Will change to bolted connection if over the value set here.
  Joist type specific setting
    Minimum shoe length
    Shoe slot diameter
    Stabilizer angle
    Stabilizer plate

## Slide 11: Joist
Joist Reports
  Bill of material for the joist
  CB - Top chord bearing length
  TCX – Chord extension and base length
Erection Views
  Shows extensions
  Section views in wire will show the joist material