## Slide 1: 2017 Member Pins
Moderator: Brian Cobb
Presenter: Ryan Vanek

## Slide 2: Member Pins
Pins will associate a members end with members or views in the Model
Added to the member end and can be edited.
Member ends can be pinned to:
  View
  Member end
  Member line
  Member plane
  It’s own plane
Pins will adjust member ends when:
  Members move
  Members are changed(Section Size)
  Member elevation changes
  Grid Lines are moved

## Slide 3: Member Pins
Auto pins that will be applied:
  Beams
    To views
    To members
    To its own plane
  Columns
    To views
  Vertical Brace
    To views
    To members
    Spliced Ends
  Horizontal Brace
    To views
    To members
    To other member plane
  Joist
    To views
    To members
    To its own plane
  Stair and Handrail
    To views
  Misc.
    To views
  Truss
    Even spaced members

## Slide 4: Member Pins
Job Setup option: Default new members to disabled restraints
  When unchecked pins will automatically get generated for most situations
  When checked pins will not automatically get generated
Colors can be setup to represent the different types of pins
  System
  User
  Disabled
Display Options: Member ends always displayed
Grid lines can now be moved

## Slide 5: Member Pins
Pin New Member Ends
  This will turn on the function if disable in setup
  There is also a toolbar icon that will show if it is disable or enabled
Auto Pin
  If pins were not generated automatically this function will apply pins to selected member ends
Pin Add
  Manually adding pins to a member end
Pin Edit
  Edit and manipulate auto or manual pins
Pin Erase
  Deletes pins that have been applied to selected members

## Slide 6: Member Pins
User pins
  Pins will become user if they are modified or added manually
Disable member pins on this end
  Pins that are disabled will be applied when the model is changed
Add
  Pins can be added from the edit screen. This is the same functionality as adding the pins manually.