## Slide 1: Reference Models and Drawings
Track 1, Thursday, 9/28/17
2:20 – 3:40
Presented by Bruce Vaughan

## Slide 2: Why Use Reference Models?
Place concrete, HVAC, plumbing, precast and other design elements in the SDS/2 detailing model.
Gets your model off to a quick start.
Helps to assure accuracy of the SDS/2 detailing model.

## Slide 3: Use Reference Models Cautiously
Accuracy may not be assured or kept up to date, especially if the contract documents are drawings.
The reference model is only usable if it was input accurately.
Perform a QC check on the reference model before proceeding!

## Slide 4: Reference Models in 7.3
In 7.3, Designlink was required to import IFC files into the model

## Slide 5: Reference Models in 7.3
Imported as reference model
Select option in Designlink window

## Slide 6: Reference Models in 2015
In 2015 and higher, SDS/2 incorporated true reference models.
Designlink no longer required to import a reference model.
Use Designlink if you need individual members.

## Slide 7: Context Menu
Modify the context (right-click) menu to be able to hide a reference model “on the fly”.

## Slide 8: Reference Model Member Line
Reference models in 7.3 are miscellaneous members with a normal member line.
Reference models beginning in 2015 no longer have a member line the user can manipulate.
A reference model is either on or off.
Reference model “member lines” can be visualized in DE erection views.

## Slide 9: Reference Model Member Line
It can sometimes be difficult to get the polygons of a reference model to appear in an erection view created by Area Save.
The reference model “member line” needs to be in the vicinity of the area save box.

## Slide 10: Reference Model Move/Rotate
The location of a reference model can easily be modified after import using Member Move.
The location and rotation can be modified using the Reference Model Manager – Refresh.
The offsets and rotations are accessible in the Reference Model Manager.

## Slide 11: Reference Drawings
2D Reference drawings can be inserted into the SDS/2 detailing model to assist in modeling input.
Architectural and structural plans and sections
Mechanical equipment cad files for support locations
Geometry layouts

## Slide 12: Reference Drawings
Reference drawings can be created from scratch in Drawing Editor.
Inserted at the current elevation and model orientation.
You can move the drawing in plan and elevation but can be awkward.
Carefully plan the saved reference point so the drawing location can easily be adjusted if needed.

## Slide 13: Reference Drawings

## Slide 14: Reference Drawings
Reference drawings cannot be placed on sheets

## Slide 15: Reference Drawings
Use “Reference Drawing Tools” to manage reference drawings in the model.

## Slide 16: Reference Model Example
SMU project concrete reference model

## Slide 17: Reference Model Example
Carthage Farm concrete, structural wood, HVAC, CLT

## Slide 18: Reference Model Example
St. David’s existing concrete and survey information

## Slide 19: Reference Model Example
St. David’s survey data model

## Slide 20: Reference Model Example
HCA Osceola existing structure from original SDS/2 model

## Slide 21: Reference Model Example
Gaylord Texan concrete

## Slide 22: Reference Model and Drawing Example
Gaylord OWP concrete, glulams, roof geometry

## Slide 23: Reference Model and Drawing Example
BSWI Exterior Façade concrete, grid alignment, slab edge geometry

## Slide 24: Reference Model and Drawing Example
Sofidel WWTP concrete and wall layout

## Slide 25: Reference Drawing Example
Hawkins Field design drawings

## Slide 26: Reference Models and Drawings
For questions and comments please inquire on the SDS/2 Detailing Forum or contact Bruce Vaughan by email: bvdet@comcast.net
Thank you for attending!