## Slide 1: Advanced Selection 101
Aaron Leacock

## Slide 2: Topics Covered
Options provided with SDS/2
Writing or modifying your own (Basics)
Selection filter by expression
Status select (New to 2017)
Selection Filter by status display
  (New to 2017)
Combining these commands with other selection lists and outputs.

## Slide 3: Benefits of Advanced Selection
A way to select items based on exact model criteria
Can generate dialogue boxes for more flexibility in one advanced selection.
Can print basic lists from the selection code
Can be easy to modify and create
Will select all that match criteria that are in the view, regardless if they are visible or not.

## Slide 4: How to find advanced selections or create your own.
Help files-
  Advanced selection examples
  Advanced selection dictionary
advanced_selection folder in your Data Directory
  Pre-written selections that you can run or use to modify.

## Slide 5: Advanced Selection
Loading an advanced selection to modify and run
  Edit> Advanced selection
Running a saved advanced selection
  Edit>Advanced selection run
Keyboard or icon shortcuts can be added through configurations

## Slide 6: Advanced selection window
Select
  This is the class of item that will be selected by the Selection Code that is entered.
Operation
  Set clears the current selection and replaces it with the selection dictated by the "Selection Code"
  Add adds to the current selection.
  Remove subtracts from the current selection.
  Toggle inverts the current selection according to the "Selection Code."

## Slide 7: Advanced selection window
Prompt
  Give you the ability to create a window prompt when running the advanced selection.
Imports and Initialization code (Not required):
  This text-entry area is for importing modules and writing initialization code. Leave this area blank unless the "Selection Code" that you are writing requires the import of a specific module or specific initialization code.
Selection Code
  This a text-entry area that defines what is to be selected.

## Slide 8: Basic Advanced Selection codes
Selecting member types
Selecting holes in members
Selecting material on members
  Use the dictionary or examples to help out
  and, or, any, all to add or restrict what is selected in the selection code
Bolts and welds are similar
  Can look in Advanced Selection Dictionary
  for attributes

## Slide 9: Basic Advanced Selection codes
Ends and Components: Basic selections.
  Currently not in help directly.
  Component selection tool can be used in conjunction with status display
    Can select by component type, and pick either the component or member
    Can be added to toolbar, right click, or keyboard shortcuts under the Model command group.

## Slide 10: Ends/Components
e.pinned == True/False
    will be based If the end it pinned or not. Disabled is considered to be pinned.
c.description == “Name”
    Name will be from the component add list
    Ex. “Beam Stiffeners – Beam” or “Outrigger”
c.graphical == True/False
    Includes Connection Components

## Slide 11: Basic Advanced Selection codes
Can select holes, welds, bolts, ends, and components based on its member’s information.
Can selection holes based on member or material information.

## Slide 12: Advanced Selection
Pre-loaded Advanced selections
  BoltDiameter.sel
  CamberSearch.sel
  Misc folder
    DefaultDialog.sel
    ConnectionTypeByMemberType.sel

## Slide 13: Selection filter by Expression
Lets you set an advanced selection to use as a selection filter to allow you pick an area of the model vs. having it select all in current view.
  Will only be able to select what is visible in the view.
  Level of Detail will also affect what can be selected
  Set Selection Filter Expression command can be added to config’s to update the by expression in the same modeling instance.

## Slide 14: Status Select
Similar to Advanced selection but uses status display window and user interface vs. written code
  Found in Model command group
Only applies to what is visible to the view
  level of detail DOES apply to what can be selected within the view.
Can select members, materials, holes, bolts, welds, connection components, and end

## Slide 15: Status Select
Only have status display information available for use.
Works just like status display to add more conditions.
  Any, All, None
Can add addition priorities to select more
  Acts like OR in Adv. selection code.

## Slide 16: Status Select Files
No differentiation between status select files and other status display files
  Up to you to keep them separated
You can load them into either area.
  Status select files will mask what it selected as a status display since there is nothing set for how to display them, it defaults to masked
  The opposite way, it defaults to select
  members since there is nothing set to be
  selected in the status display files.

## Slide 17: Select by Status Display
Similar to by expression, for advanced selection, but based on status select files
  Requires model selection after running

## Slide 18: Using these Tools
Advanced Selection / Status Select
  Use it to create selections in modeling that you can then apply to other models and selection lists like CNC, reports, etc.
  Makes the selections base on criteria vs material marks, like a selection list that was saved. So can be used on any project.
  Have some specific selections that you need to make saved as an advanced selection, or status select, to be able to make those selection on other jobs.

## Slide 19: Status display files
Can now use status display to mask or color code the selection lists.
Gives you access to much more information than hide options.
  Custom properties
  Member/Material/bolt/hole information